## Slide 1: Houston’s Future
Regional Express Transit
Regional Transit Coordination Subcommittee
10.10.19

## Slide 2
Congestion
2
Notes: Congestion Drains Society’s Resources:
- Peoples’ time
- Businesses access to employees.
Annual Delay per Houston Auto Commuter
- 53 hours in 2007
- 75 hours in 2017
Delta of 22 hours in one decade
Increase of 41.5%

## Slide 3
Future Pain Points
3
Area | 2015 Pop | 2040 Pop | % Change
CBD | 5,501 | 12,927 | 135%
IH-610 | 505,413 | 583,872 | 16%
BW 8 | 1,680,851 | 2,166,884 | 29%
SH-99 | 2,932,889 | 4,308,476 | 47%
Beyond 99 | 1,327,857 | 2,485,284 | 87%
Notes: — Region continues growing and changing.
— Population/Employment continue spreading outwards
=> Increasing demand on our transportation network
— METRO Service Area: + 2 million residents, 50%
— Regionally: + 3.1 million residents, + 48%
— As the population shifts, so do the employment centers

## Slide 4
CONNECT ACTIVITY CENTERS
4
Notes: — Multiple Major Employment Centers
— Top 9 employment centers within the City of Houston
— Employment ranges from approximately 160,000 – 25,000
— How can we connect them all?

## Slide 5
3
Park & Ride Facilities
Notes: METRO has substantially invested in the Park & Ride system
(2017) METRO Park & Rides served > 31,000 riders per weekday
METRO : 27 Park & Rides
FBCT : 4 Park & Rides
TWT: 3 Park & Rides
Pearland: 1 Park & Ride
Conroe: 1 Park & Ride

## Slide 6
Park & Ride Facilities
6
Notes: With P&R facilities throughout METRO’s Service area and beyond
Our region already has a robust Commuter Transit System!
People Fail to Recognize b/c Service does not stand out
To Increase awareness => We Must Change the Optics

## Slide 7
Proposed System
REGIONAL TRANSIT
7
Notes: Re-envisioned the existing Park & Ride system as rail
Rethink the existing commuter network to increase:
Clarity
Consistency
Visibility

## Slide 8
All-Day Base Service - Local Fare
Peak Commuter Service - Premium Fare
REGIONAL EXPRESS BUS SERVICE
8
Notes: Uniform Base Service along All Corridors:
Bi-directional service
Connecting all the TCs, PRs, & Job Centers (3 to 5 stops)
Operating 7 days a week with consistent service span
Headways of at least every 30 minutes on weekdays
Hourly in the late evenings and on weekends
Base Service = Local Fare $1.25 trips
» Transform the Local Bus Network into Regional Transit Service
» Serve the regions many employment centers
Direct Commuter Service would still exist during Peak Periods
From high demand P&Rs straight to job centers
Direct Service => Premium Fare (Current P&R fee schedule)
Maintaining the Park & Ride service that many know and love

## Slide 9
REGIONAL EXPRESS BUS SERVICE
Distinctive Branding
9
Notes: Distinctive Unique Branding => Immediate Visibility
Obvious to Newcomers to the:
Region
Neighborhoods
Employment Centers

## Slide 10
REGIONAL EXPRESS BUS SERVICE
Unique Unified Identity
10
Notes: Unified System Opportunities:
Shared Branding Across Transit Operators
Integrating other commuter services into the system
METRO MAX + TWT MAX + FBCT MAX
=> MAX Regional Express Bus Service
Shared Simple & Intuitive Labeling on Stops & Signage

## Slide 11
Extensive HOV Lanes
11
Over 25.4 million users in 2017
Notes: METRO operates 110 miles of the region’s HOV lanes
25.4 million people used METRO HOV/HOT lanes in 2017

## Slide 12
MaX Lanes
12
Notes: TxDOT has embraced the concept of MaX Lanes
Goal: “move the maximum number of people at maximum speed”
Two Way HOV/HOT Lanes, Along Every Corridor, Operating 24/7
As “peak periods” continue to grow, so do the benefits of 24/7 HOV

## Slide 13
Planned HOV Expansions
13
Notes: Numerous Expansions HOV/HOT are planned by 2040
Objective: Make HOV Bi-directional Wherever Possible
MAX-imize the advantages of existing and planned HOV/HOT lanes

## Slide 14
MAX is:
New Service
New Branding
New Fares
New Infrastructure
REGIONAL EXPRESS BUS SERVICE
14
Scalable
Affordable
Inclusive
Adaptable
Framework to Change the Service Paradigm
Notes: MAX is:
New service: 2-way, all day, every day, on every freeway
New branding: distinct, intuitive, coherent/consistent information
New fares: the base service integrates with the local bus network
New infrastructure: 2-way HOT/HOV lanes and new transit centers
Getting started is as Easy as 1, 2, 3
New service, branding, and fares can be instituted immediately
New infrastructure implemented incrementally, improving service

## Slide 15
  Referendum on November 5, 2019
15
Notes: Urgency: Referendum must pass to maintain current transit share.
$7.5 billion is really just a drop in the bucket.

## Slide 16
Autonomous Vehicles
Immediate Future: Platooning
16
Notes: One driver operates multiple vehicles linked by wireless communications. Future of Transit.

## Slide 17
Autonomous Vehicles
Driverless AV Bus operations will be possible on Houston’s HOV Lanes within the next five years
17

## Slide 18
Autonomous Vehicles
Houston is Uniquely Positioned to
Lead the AV Transit Revolution
18

## Slide 19
3
Thank you!
Katrina Bayer
Transportation Planning Manager
Central Houston, Inc.
kbayer@centralhouston.org
Notes: Any questions?

## Slide 20
Centralhouston.org